CVEN 5322: Fundamentals of Air Quality
Assignment 3
Due: Dec 2nd 2024
___________________________________________________________________________________

1. A restaurant has a dining area that is 10 m in length, 10 m in width and 3 m in height. The HVAC system provides an air exchange rate of 5 exchanges per hour. The restaurant kitchen uses a LPG stove that emits 0.2 g of NOx and 0.0002 g of SOx per second. If the restaurant operates for 12 hours a day (10 AM- 10 PM) and is closed for the remaining time. Compute the concentration of NOx and SOx in the restaurant. The restaurant has an average of 50 customers per hour State your assumptions. The half-life of NOx is roughly 50 min and that of SOx is 1 hour 15 minutes (most of the NOx and SOx are removed by adsorption to the walls and other surfaces). Assume the ambient outdoor air has a NOx concentration of 50 ppb and SOx is 0.5 ppb.

2. The average number of customers varies during the 12 hours as shown below. Develop concentration profiles assuming the emission rate is proportional to the number of customers. Use the values provided in the above example for 50 customers and scale appropriately

Hour	Customers
10- 11	20
11-12	50
12-1	80
1 - 2	50
2 - 3	40
3 - 4	20
4 - 5	30
5 - 6	120
6 - 7	100
7 - 8	70
8- 9	40
9 - 10	30

3. A carpeted area of 80 sq. m in a commercial establishment that is 10 m long, 10 m wide and 3 m tall emits formaldehyde (HCHO). The emission rate is 0.05 mg/m²·h at 22°C, increasing by 2% per degree above 22°C, and decreasing by 1% per degree below 22°C. The temperature in the establishment are as follows:
Morning – 6 hours – 10o C
Afternoon – 6 hours – 25 oC
Evening – 6 hours – 22 oC
Night – 6 hours – 15 oC

Compute the concentration of HCHO in a glass of water left in the room. The Henry's Law constant = 5020 M/atm at 293 C and the temperature dependence is given by the Arrhenius equation as follows:
ln H = (6423 ± 542)/T − (13.4 ± 2.0) (per Allou et al., 2011; Atm.Env. 45, 2991-2998).